## Slide 1: NetCrafter Tailoring Network Traffic for Non-Uniform Bandwidth Multi-GPU Systems
Amel Fatima1
Yang Yang1, Yifan Sun2, Rachata Ausavarungnirun3, and Adwait Jog1
1
2
3
Notes: Hi Everyone, my name is Yang Yang and today, I will present our work “NetCrafter, Tailoring Network Traffic for Non-Uniform Bandwidth Multi-GPU Systems”
This work is a result of a collaborative effort between the University of Virginia, William & Mary, and King Mongkut’s University of Technology North Bangkok.

## Slide 2: SUMMARY
Problem and Motivation
Multi-GPU systems accelerate workloads by interconnecting multiple GPUs
These interconnects often exhibit non-uniform bandwidth as systems scale
Slower links become performance bottlenecks, limiting scalability
Key Ideas
Target slower bandwidth links with two key strategies:
  Reduce network traffic
  Manage network traffic more efficiently
We propose NetCrafter, a network crafting engine that:
  Stitches partially empty flits to improve flit utilization
  Trims network packets with redundant data
  Sequences network traffic to prioritize latency-critical packets
Performance
Up to 64% faster, and 16% average speedup over baseline non-uniform multi-GPU setups
GPU 4
GPU 5
Infinity Fabric GPU-GPU (50+50 GB/s)
GPU 2
GPU 3
GPU 7
GPU 6
GPU 0
GPU 1
Notes: I’ll start by briefly summarizing our work.
Modern multi-GPU systems accelerate workloads by interconnecting multiple GPUs. However, as these systems scale to meet increasing demands of emerging workloads, they typically exhibit non-uniform interconnect bandwidth. In such setups, slower links often become performance bottlenecks, limiting overall scalability.
<click> To address this challenge, our goal is to optimize performance over these slower links by reducing and efficiently managing network traffic—ultimately improving bandwidth utilization where it is most constrained.
To this end, we propose NetCrafter, a network crafting engine that:
Stitches partially empty flits to improve utilization Trims redundant data from network packets, and
Sequences network traffic to prioritize latency-critical packets.
<click> With these optimizations, NetCrafter delivers up to 64% performance improvement, and 16% on average, over a baseline multi-GPU system with non-uniform interconnect bandwidth.

## Slide 3: OUTLINE
BACKGROUND AND MOTIVATION
OBSERVATIONS & KEY IDEAS
NETCRAFTER DESIGN
EVALUATION
CONCLUSION
GOAL
Notes: This is a brief outline of today’s talk

## Slide 4: OUTLINE
BACKGROUND AND MOTIVATION
OBSERVATIONS & KEY IDEAS
NETCRAFTER DESIGN
EVALUATION
CONCLUSION
GOAL
Notes: I’ll start by providing some background and then motivating our work

## Slide 5: BACKGROUND
GPUs are used to accelerate a wide range of applications
https://www.cerebras.net/blog/harnessing-the-power-of-sparsity-for-large-gpt-ai-models
ChatGPT
Graph Processing
DNN
AR/VR
Genomics
HPC Workloads
Rising application demands outgrow single-GPU capabilities
Notes: GPUs today drive everything from graph processing and deep learning to VR, HPC, genomics—and even large language models like ChatGPT.
<click>While GPUs accelerate these applications, the compute and memory demands of such workloads also continue to grow rapidly as depicted by this figure.
For example, —GPT-3 alone demands thousands of gigabytes of memory and petaflop-days of training.
<click> Clearly, a single GPU can no longer meet these skyrocketing demands - highlighting the limitations of standalone single-GPU capabilities.

## Slide 6: MULTI-GPU SYSTEMS TO THE RESCUE
Multiple GPUs are connected over high bandwidth interconnects to scale:
Compute by harnessing collective compute power of multiple GPUs
Memory by pooling memory across GPUs for a larger memory space
GPU 2
GPU 0
GPU 1
GPU 3
Notes: That’s where multi-gpu systems come to the rescue;
<click> By connecting multiple GPUs over high-speed interconnects, these systems overcome the limitations of a single GPU by scaling
<click> compute using collective computation power of multiple GPUs and processing large scale data in parallel
<click> and memory by pooling memory across GPUs for a larger memory space
<click>This is exactly what commercial systems like NVIDIA DGX, AMD Mi300X, and Intel XE deliver with their multi-GPU setups.

## Slide 7: SCALING MULTI-GPU SYSTEMS
Multi-GPU systems must scale with growing application demands
These systems typically scale in a hierarchical manner
  Tightly coupled (e.g., MCM style): Linked via higher-bandwidth interconnects
  Loosely coupled (e.g., Multi-GPU style): Connected over lower-bandwidth interconnects
Multi-GPU scaling typically introduces bandwidth non-uniformity
(e.g., Frontier, Summit, Aurora)
GPU 0
GPU 1
GPU 4
GPU 5
GPU 6
GPU 7
GPU 2
GPU 3
Notes: However, Multi-GPU systems must continue to scale with the growing demands of modern applications.
<click> As we scale beyond a single GPU cluster, systems typically adopt a hierarchical interconnect design—
<click>with fast, high-bandwidth links connecting nearby GPUs
<click> and slower, lower-bandwidth links connecting distant ones
<click> This hierarchy introduces non-uniform bandwidth across all GPUs, creating new bottlenecks as the system scales. Now, lets take a look at the repercussions of this non-uniform bandwidth on our multi-GPU system.

## Slide 8: NON-UNIFORM BANDWIDTH -> NUMA
GPU 5
GPU 4
GPU 7
GPU 6
GPU 2
GPU 3
GPU 0
GPU 1
Memory access bandwidth varies across the system
SIMD
COMPUTE UNIT
SIMD
SIMD
SIMD
Coalesce
x
Wavefront
address
0x0
0x4
0x8
tid
0
1
2
3
SIMD
0xC
Coalesce
64-BYTE CACHE LINE REQUEST
0x0
OFFSET
RDMA Engine
L1 TLB
L1 $
Shared
L2 TLB
Shared L2 Cache
HBM
Page Walker
PWC
GMMU
Notes: Non-uniform bandwidth across GPU links creates a NUMA-style system
<click> where remote accesses cost far more than local ones.
To understand how this works, lets take a closer look <click> into our GPU architecture to observe a single GPU’s memory access path:
<click> SIMD Wavefronts issue fine-grained loads and stores.
<click> Coalescing logic merges accesses into 64-byte cache-line requests.
<click> These flows hit the L1 TLB and L1 data cache, then pass through the GMMU (page walker and PWC) into the shared L2 cache backed by HBM.
<click> Finally, any access that misses and targets remote memory is handed off to the RDMA engine for a peer-GPU fetch.
With that microarchitecture in mind, you can see how remote accesses over slower links will amplify latency and throttle bandwidth

## Slide 9: NON-UNIFORM BANDWIDTH -> NUMA
GPU 5
GPU 4
GPU 7
GPU 6
GPU 2
GPU 3
GPU 0
GPU 1
SIMD
COMPUTE UNIT
SIMD
SIMD
SIMD
Coalesce
x
Wavefront
address
0x0
0x4
0x8
tid
0
1
2
3
SIMD
0xC
Coalesce
64-BYTE CACHE LINE REQUEST
0x0
OFFSET
RDMA Engine
L1 TLB
L1 $
Shared
L2 TLB
Shared L2 Cache
HBM
Page Walker
PWC
GMMU
Memory access bandwidth varies across the system
Nearby GPUs enjoy higher bandwidth and lower latency, and vice versa
Notes: <click> Nearby GPUs enjoy higher bandwidth and lower latency,

## Slide 10: NON-UNIFORM BANDWIDTH -> NUMA
Memory access bandwidth varies across the system
Nearby GPUs enjoy higher bandwidth and lower latency, and vice versa
GPU 5
GPU 4
GPU 7
GPU 6
GPU 2
GPU 3
GPU 0
GPU 1
SIMD
COMPUTE UNIT
SIMD
SIMD
SIMD
Coalesce
x
Wavefront
address
0x0
0x4
0x8
tid
0
1
2
3
SIMD
0xC
Coalesce
64-BYTE CACHE LINE REQUEST
0x0
OFFSET
RDMA Engine
L1 TLB
L1 $
Shared
L2 TLB
Shared L2 Cache
HBM
Page Walker
PWC
GMMU
Notes: and far GPUs experience lower bandwidth and higher latency

## Slide 11: NON-UNIFORM BANDWIDTH -> NUMA
Non-uniform bandwidth multi-GPU systems are constrained by:
  Slower bandwidth interconnects connecting the GPUs
Chart: 
| GUPS | MT | MIS | IM2COL | ATAX | BS | MM2 | MVT | SPMV | PR | SR | SYR2K | LENET | RNET18 | VGG16 | Gmean
Some GPUs connected via slower links | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
All GPUs connected via high-speed links | 1.7322 | 1.5764 | 1.8608 | 2.3019 | 1.0205 | 1.9095 | 1.2688 | 1.1447 | 1.1248 | 1.0109 | 1.8497 | 1.0165 | 1.4632 | 2.0766 | 1.7106 | 1.4827
Non-uniform bandwidth causes up to 2.3× slowdown in GPU performance
Higher is better
Notes: To quantify the impact of non-uniform bandwidth on application performance—
<click> This figure shows performance across different multi-GPU setups. Each red bar represents a run where some GPU pairs are connected via slower links, while the green bar shows the ideal case with all GPUs connected via high-speed links.
<click> As you can see, slower links introduce significant slowdowns— with IM2COL suffering up to a 2.3× drop in performance.
This clearly motivates smarter traffic crafting across slower links

## Slide 12
Slower interconnects lead to performance bottlenecks. How can we minimize the impact of non-uniform bandwidth in emerging multi-GPU systems?
Notes: That brings us to the key challenge of this work : slower interconnects create performance bottleneck-Therefore how can we minimize the impact of this non-uniform bandwidth in our next-generation multi-GPU systems?

## Slide 13: OUTLINE
BACKGROUND AND MOTIVATION
OBSERVATIONS & KEY IDEAS
NETCRAFTER DESIGN
EVALUATION
CONCLUSION
GOAL
Notes: To address that challenge, our goal is pretty straight forward

## Slide 14: GOAL
Optimize slower bandwidth links:
Reducing network traffic across these links
Efficiently managing network traffic across these links
Notes: which is to optimize slower links by
<click>Reducing the amount of traffic, and
<click>Efficiently Managing the network traffic that remains.

## Slide 15: OUTLINE
BACKGROUND AND MOTIVATION
OBSERVATIONS & KEY IDEAS
NETCRAFTER DESIGN
EVALUATION
CONCLUSION
GOAL
Notes: To achieve that goal, we make a few observations and propose our three main key ideas

## Slide 16: Transmitting packets across the network
Network Transfer through Flits
Flit = fixed-size unit (x bytes), sent per cycle
Basic granularity of data transfer in interconnects
GPU packet breakdown
Packet = Header + Payload
Split into flits (fixed-size units)
Empty bytes padded to align the last flit with flit size
Flit
GPU request Packet
Header
Payload
Transmitted to network
Notes: Before we dive into our observations, let’s see how GPUs send data over network.
<click> Network transfers happen in the granularity of a flit which is the smallest unit of data that can be sent across the network. <click> Each GPU request becomes a packet WHICH IS composed of a header that contains <click> the metadata to route the request over the network and the payload which is the actual data that needs to be sent over the network
<click>The packet is then split into fixed sized flits before being transmitted to the network.
<click>If the packet size is not a multiple of the flit size, the flit is padded with empty bytes to align to the flit size. <click>And then finally the flits are sent across the network

## Slide 17: OBSERVATION #01
Inefficient Flit Utilization Due to Padding
  Flits contain substantial empty bytes
  These empty bytes are padded with redundant data
  Redundant data increases unnecessary network load
Each packet type contributes differently to this network load
  Read Req (Header + Address)
  Write Req (Header + Data + Address)
  Page Table Req (Header +Address)
Write Req
Read Rsp
Write Rsp
Read Req
Page Table Req
Page Table Rsp
  Read Rsp (Header + Data)
  Write Rsp (Header)
  Page Table Rsp (Header + Address)
Empty
Packet Type
Shape
Notes: Now LETS discuss our first observation which is <click>Inefficient flit utilization due to padding. As we discussed: <click> Flit contain empty bytes <click> which are padded with redundant data before being transmitted
<click> this redundant data increases uneccesary network load
<click>We further observed that there are different packet types in such network links, <click until finish>, those packets have different sizes and therefore different padding granularities
If you look at the breakdown by packet type, you’ll see that read requests and page-table responses send mostly header flits (small payloads) padded out to full size.
Write requests and read responses fare slightly better, but still pad their last flit.

## Slide 18: OBSERVATION #01
Different packet types introduce varying padding overhead
Chart: 
| GUPS | MT | MIS | IM2COL | ATAX | BS | MM2 | MVT | SPMV | PR | SR | SYR2K | LENET | RNET18 | VGG16
Flits 75% padded | 3353292 | 131616 | 1455685 | 1568482 | 662434 | 787904 | 1160324 | 803104 | 21914727 | 1402588 | 4194656 | 2144437 | 388749 | 2325918 | 1229166
Flits 25% padded | 5657904 | 213794 | 2157671 | 1603028 | 685190 | 813284 | 1908215 | 820150 | 51889025 | 3949798 | 4332368 | 4887794 | 406745 | 2418841 | 1368946
No padding | 13413168 | 526464 | 5822740 | 6273928 | 2649736 | 3151616 | 4641404 | 3212416 | 87658908 | 5610352 | 16778624 | 8577788 | 1554996 | 9303672 | 4916664
Percentage of Total Flits
Write Req
Read Rsp
Write Rsp
Read Req
Page Table Req
Page Table Rsp
Packet Type
Shape
%Padded
25%
75%
25%
25% + No padding
25% + No padding
25%
Notes: we see each packet type pads a different fraction of its last flits as shown below <click until finish>
<click> We further evaluated different workloads to see the percentage of flits which had redundant bytes padded to them, as shown in the figure

## Slide 19: OBSERVATION #01
Different packet types introduce varying padding overhead
Chart: 
| GUPS | MT | MIS | IM2COL | ATAX | BS | MM2 | MVT | SPMV | PR | SR | SYR2K | LENET | RNET18 | VGG16
Flits 75% padded | 3353292 | 131616 | 1455685 | 1568482 | 662434 | 787904 | 1160324 | 803104 | 21914727 | 1402588 | 4194656 | 2144437 | 388749 | 2325918 | 1229166
Flits 25% padded | 5657904 | 213794 | 2157671 | 1603028 | 685190 | 813284 | 1908215 | 820150 | 51889025 | 3949798 | 4332368 | 4887794 | 406745 | 2418841 | 1368946
No padding | 13413168 | 526464 | 5822740 | 6273928 | 2649736 | 3151616 | 4641404 | 3212416 | 87658908 | 5610352 | 16778624 | 8577788 | 1554996 | 9303672 | 4916664
Percentage of Total Flits
Write Req
Read Rsp
Write Rsp
Read Req
Page Table Req
Page Table Rsp
Packet Type
Shape
%Padded
25%
75%
25%
25% + No padding
25% + No padding
25%
~40% of flits in the network are padded with 25–75% useless data
Notes: Overall, we observed that around ~40% of all flits in the network are padded with either 25%~75% redundant bytes.

## Slide 20: KEY IDEA I: STITCHING
Stitch flits across request categories to reduce network traffic overhead
Read Rsp
PT Req
Read Rsp
Write Rsp
PT Rsp
Write Req
Write Rsp
Read Req
Notes: This brings us to our first key idea which is Stitching, We propose to Intelligently Stitch flits across request categories to reduce the total network traffic overhead. <click>This figure depicts a few network packets traversing the network. For better understanding, lets do a walk through of our stitching approach assuming these packets traversing the slower links

## Slide 21: KEY IDEA I: STITCHING
Read Rsp
PT Req
Read Rsp
Write Rsp
PT Rsp
Write Req
Write Rsp
Read Req
Stitch flits across request categories to reduce network traffic overhead
Notes: As discussed, we can stitch flits across different packet types when its appropriate,
Based on the empty bytes each network flit has, we intelligently stitch different flits together.
<click> E.g., read response packet can completely get rid of its last flit if the content is stitched with another read response flit. <click>

## Slide 22: KEY IDEA I: STITCHING
Read Rsp
PT Req
Read Rsp
Write Rsp
PT Rsp
Write Req
Write Rsp
Read Req
Stitch flits across request categories to reduce network traffic overhead
Notes: Similarly, here write response flit <click> can stitch its payload data with a preceding page table request flit to get rid of one more flit in the network.

## Slide 23: KEY IDEA I: STITCHING
Read Rsp
PT Req
Read Rsp
Write Rsp
PT Rsp
Write Req
Write Rsp
Read Req
Stitch flits across request categories to reduce network traffic overhead
Notes: Here page table response flit <click> can stitch its payload data with a write response flit

## Slide 24: KEY IDEA I: STITCHING
Read Rsp
PT Req
Read Rsp
Write Rsp
PT Rsp
Write Req
Write Rsp
Read Req
Stitch flits across request categories to reduce network traffic overhead
Notes: Again, write response flit <click> can stitch its flit data with a read response flit

## Slide 25: KEY IDEA I: STITCHING
Read Rsp
PT Req
Read Rsp
Write Rsp
PT Rsp
Write Req
Write Rsp
Read Req
Stitch flits across request categories to reduce network traffic overhead
Notes: And finally the read request flit <click> stitches its flit data with a write response flit together.

## Slide 26: KEY IDEA I: STITCHING
Read Rsp
PT Req
Read Rsp
Write Rsp
PT Rsp
Write Req
Write Rsp
Read Req
Stitch flits across request categories to reduce network traffic overhead
Notes: All in all, we are able to get rid of a total of five flits <click> from the network.

## Slide 27: KEY IDEA I: STITCHING
Stitch flits across request categories to reduce network traffic overhead
Notes: click

## Slide 28: KEY IDEA I: STITCHING
Network Traffic Reduced
Stitch flits across request categories to reduce network traffic overhead
Notes: <click> This helps reduce the total traffic over the slower network links and improve bandwidth utilization.
Details on the decision logic for flit stitching, the required packet structure modifications, and the un-stitching mechanism at the receiver are discussed in the paper. Please refer to it for more information.

## Slide 29: OBSERVATION #02
Prefetched unused data wastes bandwidth
Notes: <click> Now lets move to our second observation: which is prefetched unused data wastes bandwidth.

## Slide 30: OBSERVATION #02
Prefetched unused data wastes bandwidth
SIMD
COMPUTE UNIT
SIMD
SIMD
SIMD
Coalesce
x
Wavefront
address
0x0
0x4
0x8
tid
0
1
2
3
SIMD
0xC
Coalesce
64-BYTE CACHE LINE READ REQUEST
RDMA Engine
L1 TLB
L1 $
Shared
L2 TLB
Shared L2 Cache
HBM
Page Walker
PWC
GMMU
GPU 5
GPU 4
GPU 7
GPU 6
GPU 6
GPU 3
GPU 0
GPU 1
Required by wavefront
Prefetched as part of cache line
Notes: <click> As discussed previously, accesses generated for the same cacheline by a wavefront are coalesced by the coalescer and issued as a single cache line request.

## Slide 31: OBSERVATION #02
Prefetched unused data wastes bandwidth
  Read response includes more data than requested
SIMD
COMPUTE UNIT
SIMD
SIMD
SIMD
Coalesce
x
Wavefront
address
0x0
0x4
0x8
tid
0
1
2
3
SIMD
0xC
Coalesce
64-BYTE CACHE LINE READ REQUEST
RDMA Engine
L1 TLB
L1 $
Shared
L2 TLB
Shared L2 Cache
HBM
Page Walker
PWC
GMMU
Required by wavefront
Prefetched as part of cache line
Read Rsp
Header
Payload
GPU 5
GPU 4
GPU 7
GPU 6
GPU 6
GPU 3
GPU 0
GPU 1
Notes: We observed that read responses may include more data than requested, which wastes network bandwidth

## Slide 32: OBSERVATION #02
Prefetched unused data wastes bandwidth
  Read response includes more data than requested
Chart: 
| GUPS | MT | MIS | IM2COL | ATAX | BS | MM2 | MVT | SPMV | PR | SR | SYR2K | LENET | RNET18 | VGG16
16 Bytes | 1456116 | 0 | 1192434 | 63 | 138002 | 0 | 305867 | 278528 | 21904045 | 58501 | 0 | 1057640 | 97064 | 843599 | 169587
32 Bytes | 10387 | 0 | 670 | 0 | 0 | 0 | 0 | 0 | 10181 | 81851 | 0 | 0 | 27501 | 486590 | 402554
48 Bytes | 0 | 0 | 39 | 26 | 0 | 0 | 0 | 0 | 5 | 306347 | 0 | 0 | 39190 | 96 | 732
Full Cacheline (64B) | 264500 | 544 | 128997 | 325518 | 524432 | 263616 | 161575 | 524576 | 496 | 955889 | 4194592 | 20864 | 130800 | 416115 | 383572
Percentage of Total
Read Requests
Most applications require ≤16B from each 64B GPU cache line
Notes: <click> Digging into traffic, we find that most applications only need 16 bytes or less from 64-byte cache line.
Yet GPUs still fetch and ship the full 64 bytes over the network

## Slide 33: KEY IDEA II: TRIMMING
Trim redundant flits to cut network overhead
Notes: This gives us our second key idea: trim away unneeded bytes so only the requested data traverses the interconnect.
An example is shown below.
When the remote GPU hosting the cache line is ready to satisfy the packet request, we analyze it to determine the exact number of bytes requested by the wavefront.
If this number is 16 bytes or fewer, and the response packet has to traverse slower network, we trim the packet <click>
Otherwise, we don’t perform trimming to maintain spatial locality.
Q: How to decide how many bytes are needed?

## Slide 34: KEY IDEA II: TRIMMING
Trim redundant flits to cut network overhead
Notes: This gives us our second key idea: trim away unneeded bytes so only the requested data traverses the interconnect.
An example is shown below.
When the remote GPU hosting the cache line is ready to satisfy the packet request, we analyze it to determine the exact number of bytes requested by the wavefront.
If this number is 16 bytes or fewer, and the response packet has to traverse slower network, we trim the packet <click>
Otherwise, we don’t perform trimming to maintain spatial locality.
Q: How to decide how many bytes are needed?

## Slide 35: KEY IDEA II: TRIMMING
Trim redundant flits to cut network overhead
Notes: This gives us our second key idea: trim away unneeded bytes so only the requested data traverses the interconnect.
An example is shown below.
When the remote GPU hosting the cache line is ready to satisfy the packet request, we analyze it to determine the exact number of bytes requested by the wavefront.
If this number is 16 bytes or fewer, and the response packet has to traverse slower network, we trim the packet
Otherwise, we don’t perform trimming to maintain spatial locality.
Q: How to decide how many bytes are needed?

## Slide 36: KEY IDEA II: TRIMMING
Trim redundant flits to cut network overhead
Notes: This gives us our second key idea: trim away unneeded bytes so only the requested data traverses the interconnect.
An example is shown below.
When the remote GPU hosting the cache line is ready to satisfy the packet request, we analyze it to determine the exact number of bytes requested by the wavefront.
If this number is 16 bytes or fewer, and the response packet has to traverse slower network, we trim the packet
Otherwise, we don’t perform trimming to maintain spatial locality.
Q: How to decide how many bytes are needed?

## Slide 37: KEY IDEA II: TRIMMING
Trim redundant flits to cut network overhead
Notes: This gives us our second key idea: trim away unneeded bytes so only the requested data traverses the interconnect.
An example is shown below.
When the remote GPU hosting the cache line is ready to satisfy the packet request, we analyze it to determine the exact number of bytes requested by the wavefront.
If this number is 16 bytes or fewer, and the response packet has to traverse slower network, we trim the packet
Otherwise, we don’t perform trimming to maintain spatial locality.
Q: How to decide how many bytes are needed?

## Slide 38: KEY IDEA II: TRIMMING
Network Traffic Reduced
Trim redundant flits to cut network overhead
Notes: This gives us our second key idea: trim away unneeded bytes so only the requested data traverses the interconnect.
An example is shown below.
When the remote GPU hosting the cache line is ready to satisfy the packet request, we analyze it to determine the exact number of bytes requested by the wavefront.
If this number is 16 bytes or fewer, and the response packet has to traverse slower network, we trim the packet
Otherwise, we don’t perform trimming to maintain spatial locality.
Our trimming approach further help to reduce network traffic

## Slide 39: OBSERVATION#03
PTW-related flits are more latency critical than other flits
Chart: 
| GUPS | MT | MIS | IM2COL | ATAX | BS | MM2 | MVT | SPMV | PR | SR | SYR2K | LENET | RNET18 | VGG16
Read PTW-Related Accesses Prioritized | 1.0442 | 0.99299 | 1.0069 | 0.9986 | 1.0117 | 0.99093 | 0.99 | 1.0633 | 1.0577 | 1.0221 | 0.99433 | 1.0113 | 1.0132 | 1.0061 | 1.0302
Data Accesses Prioritized | 0.97326 | 0.94939 | 0.86853 | 0.99683 | 0.99537 | 1.0007 | 0.99277 | 0.98407 | 0.75902 | 0.98394 | 1.0005 | 0.97626 | 0.98795 | 1.0064 | 0.98534
Speedup Normalized to
Non-uniform BW Configuration
Higher is better
Notes: <click> Our third observation shows that page-table walker (PTW) traffic is more sensitive to latency than data.
We ran two experiments under non-uniform links: <click>
one where we prioritize PTW-related flits (green bars) and one where we prioritize data flits (blue bars).
In almost every benchmark, giving PTW flits the lead yields higher speedups
This tells us: to reduce stalls and page-fault penalties, we should sequence PTW-related packets ahead of regular data on slow links.
(same number of data to be prioritized)

## Slide 40: KEY IDEA III: SEQUENCING
Prioritize flits in flight so latency-critical packets lead the line on slow links
Notes: Based on this observation, we propos our final key idea which is sequencing.
We propose to Prioritize flits in flight so latency-critical packets lead the line on slow links

## Slide 41: KEY IDEA III: SEQUENCING
Execution Time Reduced
Prioritize flits in flight so latency-critical packets lead the line on slow links
Notes: This will help to reduce execution time

## Slide 42: PUTTING IT TOGETHER
Execution Time Reduced
Network Traffic Reduced
Network Traffic Reduced
  Stitching
  Trimming
  Sequencing
42
Reducing network traffic across these links
Efficiently managing network traffic across these links
Notes: Putting it together, NetCrafter’s stitching, trimming, and sequencing work to slash unnecessary flits, eliminate wasted data, and accelerate critical traffic on slow links.
Which satisfy our goals.

## Slide 43: OUTLINE
BACKGROUND AND MOTIVATION
OBSERVATIONS & KEY IDEAS
NETCRAFTER DESIGN
EVALUATION
CONCLUSION
GOAL
Notes: Now, we’ll dig deeper into NetCrafter design details

## Slide 44: Mechanism: NetCrafter
Each cluster switch includes an integrated NetCrafter controller
NetCrafter Controller
Notes: Our NetCrafter controller contains our Stitching, Trimming and Sequencing engine and is integrated within each cluster’s switch.

## Slide 45: Mechanism: NetCrafter
Each cluster switch includes an integrated NetCrafter controller
Cache Line
(64B)
Trim Engine
NetCrafter Controller
Notes: The packet come into the switch

## Slide 46: Mechanism: NetCrafter
Each cluster switch includes an integrated NetCrafter controller
Cache Line
(64B)
MUX 0
pkt.trim
Trim Engine
NetCrafter Controller
Notes: We first check whether the trim signal is enabled

## Slide 47: Mechanism: NetCrafter
Each cluster switch includes an integrated NetCrafter controller
Decide the granularity
Cache Line
(64B)
MUX 0
pkt.trim
16B
Trim Engine
NetCrafter Controller
Notes: If yes, we then trim the packets and send it to the next stage for stitching

## Slide 48: Mechanism: NetCrafter
flit.empty_bytes
MUX 1
pkt.dst + pkt.type
CQ.type(s)
MUX 2
Per CQ.dst
Cache Line
(64B)
MUX 0
pkt.trim
16B
Trim Engine
Decide the granularity
Choose the stitching candidates
NetCrafter Controller
Each cluster switch includes an integrated NetCrafter controller
Notes: The stitch logic contain a cluster queue (CQ) structure, which is partitioned per destination and per type.
Packets will be enqueued and then wait for selection

## Slide 49: Mechanism: NetCrafter
flit.empty_bytes
MUX 1
pkt.dst + pkt.type
CQ.type(s)
MUX 2
Per CQ.dst
Cache Line
(64B)
MUX 0
pkt.trim
16B
Trim Engine
Decide the granularity
Choose the stitching candidates
Flit to Stitch
Candidate
Stitching Engine
NetCrafter Controller
Each cluster switch includes an integrated NetCrafter controller
Notes: We will run stitch candidate searching to find two flits to be stitched, more details of this algorithm can be found in the paper

## Slide 50: Mechanism: NetCrafter
flit.empty_bytes
MUX 1
pkt.dst + pkt.type
CQ.type(s)
MUX 2
Per CQ.dst
Cache Line
(64B)
MUX 0
pkt.trim
16B
Trim Engine
Decide the granularity
Choose the stitching candidates
Flit to Stitch
Candidate
Stitching Engine
Size
ID
type
Packet support + Sequence
Stitched Flit
NetCrafter Controller
Each cluster switch includes an integrated NetCrafter controller
Notes: And once the candidate is there, we will inject a small header if required into the flit to support correct unstitching at the target. The stitched flits are then ready to be shipped or sent back to the multiplexer for another chance of stitching.

## Slide 51: Mechanism: NetCrafter
flit.empty_bytes
MUX 1
pkt.dst + pkt.type
CQ.type(s)
MUX 2
Per CQ.dst
Cache Line
(64B)
MUX 0
pkt.trim
16B
Trim Engine
Flit to Stitch
Candidate
Stitching Engine
Size
ID
type
NetCrafter Controller
Stitched Flit
CQ.timer.set
CQ.timeout
Activate
Sequencing
Scheduler
select
found?
Flit Pooling (please check the paper!)
Each cluster switch includes an integrated NetCrafter controller
Notes: To further optimize stitching, we designed a flit pooling process to allow more opportunities for stitching, please check the paper for more details.

## Slide 52: OUTLINE
BACKGROUND AND MOTIVATION
OBSERVATIONS & KEY IDEAS
NETCRAFTER DESIGN
EVALUATION
CONCLUSION
GOAL
Notes: Now, we will talk about our setup and evaluation

## Slide 53: METHODOLOGY
MGPUSim Simulator:
Design points:
  Baseline: non-uniform bandwidth configuration without NetCrafter
  Sector Cache: baseline configuration with sector cache
  NetCrafter: non uniform system with Stitching, Trimming & Sequencing
Compute Unit | 1GHz, 64 per GPU (4 GPUs in total)
L1 D/I, L2 cache | 64/32KB, 4MB per GPU (shared)
Heterogeneous Interconnect | Inter-GPU-cluster - 16GBps, bi-directional Intra-GPU-cluster - 128GBps, bi-directional
CTA/Page Scheduling | LASP (Locality-Aware Scheduling and Placement)
NetCrafter Parameters | Cluster Queue - 1024 Entries (16B each)
Notes: We use MGPUSim to implement NetCrafter, and we simulate a 4-GPU setup. Detailed configurations are shown below
We evaluate on 3 design points: the baseline, a sector cache one, and then NetCrafter one

## Slide 54: NetCrafter vs. Baseline
Speedup Normalized to
non-uniform BW Configuration
Chart: 
| GUPS | MT | MIS | IM2COL | ATAX | BS | MM2 | MVT | SPMV | PR | SR | SYR2K | LENET | RNET18 | VGG16 | Gmean
Stitching | 1.1023 | 1.1344 | 1.1377 | 1.2142 | 1.0052 | 1.1379 | 1.0582 | 1.0069 | 1.056 | 1.0156 | 1.1208 | 1.0036 | 1.0483 | 1.1555 | 1.0953 | 1.0843
Trimming | 1.1417 | 1 | 1.5454 | 1.0006 | 0.9971 | 1 | 1.0467 | 0.99388 | 1.119 | 0.9988 | 1 | 1.0059 | 0.98826 | 1.1669 | 1.0287 | 1.0613
Stitching + Trimming | 1.2238 | 1.1344 | 1.6091 | 1.2088 | 1.0027 | 1.1379 | 1.0825 | 1.0177 | 1.1198 | 1.0055 | 1.1207 | 1.0093 | 1.0458 | 1.3636 | 1.1243 | 1.1378
Stitching + Trimming + Sequencing | 1.3714 | 1.1086 | 1.6413 | 1.2175 | 1.0137 | 1.1296 | 1.0996 | 1.0658 | 1.1278 | 1.0227 | 1.1156 | 1.015 | 1.0521 | 1.3815 | 1.147 | 1.1567
16% Speedup
Higher is better
NetCrafter provides 16% speedup on average
1.64x
Notes: Here are our results
NetCrafter with all three mechanisms provides 16% speedup on average, with a maxium speedup of 1.64 times.

## Slide 55: NetCrafter vs. Baseline
Chart: 
| GUPS | MT | MIS | IM2COL | ATAX | BS | MM2 | MVT | SPMV | PR | SR | SYR2K | LENET | RNET18 | VGG16 | Gmean
Stitching | 1.1023 | 1.1344 | 1.1377 | 1.2142 | 1.0052 | 1.1379 | 1.0582 | 1.0069 | 1.056 | 1.0156 | 1.1208 | 1.0036 | 1.0483 | 1.1555 | 1.0953 | 1.0843
Trimming | 1.1417 | 1 | 1.5454 | 1.0006 | 0.9971 | 1 | 1.0467 | 0.99388 | 1.119 | 0.9988 | 1 | 1.0059 | 0.98826 | 1.1669 | 1.0287 | 1.0613
Stitching + Trimming | 1.2238 | 1.1344 | 1.6091 | 1.2088 | 1.0027 | 1.1379 | 1.0825 | 1.0177 | 1.1198 | 1.0055 | 1.1207 | 1.0093 | 1.0458 | 1.3636 | 1.1243 | 1.1378
Stitching + Trimming + Sequencing | 1.3714 | 1.1086 | 1.6413 | 1.2175 | 1.0137 | 1.1296 | 1.0996 | 1.0658 | 1.1278 | 1.0227 | 1.1156 | 1.015 | 1.0521 | 1.3815 | 1.147 | 1.1567
16% Speedup
Reduces network traffic
Efficiently manages network traffic
Higher is better
Speedup Normalized to
non-uniform BW Configuration
NetCrafter provides 16% speedup on average
1.64x
Notes: And we evaluated different combinations of our mechanism, for example, stitching+trimming could reduce network traffic, while sequencing can efficiently manage network traffic

## Slide 56: NetCrafter vs. Baseline + Sector Cache
Chart: 
| GUPS | MT | MIS | IM2COL | ATAX | BS | MM2 | MVT | SPMV | PR | SR | SYR2K | LENET | RNET18 | VGG16 | Gmean
Stitching | 1.1023 | 1.1344 | 1.1377 | 1.2142 | 1.0052 | 1.1379 | 1.0582 | 1.0069 | 1.056 | 1.0156 | 1.1208 | 1.0036 | 1.0483 | 1.1555 | 1.0953 | 1.0843
Sector Cache Baseline (16B) | 1.1424 | 0.93021 | 1.4917 | 0.94116 | 0.91617 | 0.666 | 0.9453 | 0.68598 | 1.1183 | 0.6106 | 0.4318 | 1.0003 | 0.8091 | 0.98712 | 0.81592 | 0.86495
Trimming | 1.1417 | 1 | 1.5454 | 1.0006 | 0.9971 | 1 | 1.0467 | 0.99388 | 1.119 | 0.9988 | 1 | 1.0059 | 0.98826 | 1.1669 | 1.0287 | 1.0613
Stitching + Trimming | 1.2238 | 1.1344 | 1.6091 | 1.2088 | 1.0027 | 1.1379 | 1.0825 | 1.0177 | 1.1198 | 1.0055 | 1.1207 | 1.0093 | 1.0458 | 1.3636 | 1.1243 | 1.1378
Stitching + Trimming + Sequencing | 1.3714 | 1.1086 | 1.6413 | 1.2175 | 1.0137 | 1.1296 | 1.0996 | 1.0658 | 1.1278 | 1.0227 | 1.1156 | 1.015 | 1.0521 | 1.3815 | 1.147 | 1.1567
Higher is better
NetCrafter provides 16% speedup on average
Speedup Normalized to
non-uniform BW Configuration
Notes: Lastly, we compare our design towards a sector cache design, where the remote cache line request is sectored. This is to show the effectiveness or our trimming mechanism.
And it's clear that our trimming mechanism outperform this sector cache design. sector is for all link

## Slide 57: More Details…
Flit Pooling and Selective Flit Pooling
Impact of trimming on cache MPKI
Modifications to the packet structure
Hardware overhead
Latency overhead
CTA/data placement
Coherence implications
Handling deadlocks
Packet unstitching details at the target
Sensitivity studies with varied :
  Flit-Pooling windows
  Bandwidth numbers and ratios
  Flit sizes
Please check our paper!
Notes: Before concluding, I’d like to highlight a few details covered in our paper but omitted here due to time constraints—such as Flit Pooling and Selective Flit Pooling, which enhance our stitching efficiency. Additional design elements, including packet structure modifications, associated overheads, and other implementation details, are also discussed in the paper. Please refer to it for a comprehensive understanding. For the switch latency:
Internally, the network components are wired to tick 12 times per cycles. With switch latency of 360, every cycle ticking 12 times, we get 30 cycles. In addition, the network components take an additional two cycles.
Hw: 0.098% of L2

## Slide 58: OUTLINE
BACKGROUND AND MOTIVATION
OBSERVATIONS & KEY IDEAS
NETCRAFTER DESIGN
EVALUATION
CONCLUSION
GOAL
Notes: Now I would like to conclude:

## Slide 59
NetCrafter, a combination of novel approaches (Stitching, Trimming and Sequencing) to deal with the multi-GPU network traffic, which provides up to 64% speedup and 16% speedup on average.
Our proposed techniques are generic and can be applied to any network. They are especially useful in alleviating the bottlenecks presented by lower-bandwidth networks connecting multiple groups of GPUs.
Conclusion
Notes: We focus on the problem of Multi-GPU system bandwidth non-uniformity.
read

## Slide 60: NetCrafter Tailoring Network Traffic for Non-Uniform Bandwidth Multi-GPU Systems
Thanks!
Questions?
Amel Fatima1, Yang Yang1, Yifan Sun2, Rachata Ausavarungnirun3, and Adwait Jog1
1
2
3
Notes: Thanks, questions are welcomed.

## Slide 61
BACKUP SLIDES

## Slide 62: Packet structure to support NetCrafter
ID
Size
Header
Type Field
Meta-data
Address
Occupied
Empty
a) A typical PCIe Packet
Unused Address Bits
Meta-data
Address
Occupied
Header
Payload
Meta-data
Address
Occupied
b) Stitching a complete packet
c) Stitching a partial packet
Payload
Payload (Partial)
Trim
3b
Trim
3b

## Slide 63: Ratio of Data vs Page Table Accesses per GPU

## Slide 64
Distribution of Memory Access Requests/GPU

## Slide 65
Cache MPKI Comparison with Sector Cache
L1 Cache MPKI Normalized to
Trimming Approach
Chart: 
| GUPS | MT | MIS | IM2COL | ATAX | BS | MM2 | MVT | SPMV | PR | SR | SYR2K | LENET | RESNET18 | VGG16
Trimming | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Sector Cache Baseline (16B) | 1.0065 | 2.5 | 1.3721 | 1.7981 | 1.1761 | 2 | 1.5931 | 1.1734 | 1.0139 | 4.521 | 4 | 1.0187 | 2.1507 | 1.8198 | 2.2803